## Slide 1
Safety Alert: Hazira gas terminal condensate release and fire, 2020
Grade: Alert
Audience: Other sites and peer organisations
Incident: Hazira gas terminal condensate release and fire · 2020-09-24
Learning purposes: not a statutory document · Learnings drafted by an AI agent from AI-assisted findings
DRAFT
Review: draft · Classification: internal · Version 1.0
Draft because: the investigation status is in progress; no finding is marked as edited by a person
Learning purposes: not a statutory document · Generated with ProbeMatrix Learnings Coach v2.0.0a7 (open source, MIT) from a ProbeMatrix four-level human-factors investigation. ProbeMatrix by Eyekyam: ashley@eyekyam.com
DRAFT
Notes: Grade: Alert
Audience: Other sites and peer organisations
Incident: Hazira gas terminal condensate release and fire · 2020-09-24
Learning purposes: not a statutory document · Learnings drafted by an AI agent from AI-assisted findings
DRAFT
Review: draft · Classification: internal · Version 1.0
Draft because: the investigation status is in progress; no finding is marked as edited by a person
Data quality and limits:
- Draft learnings from an unreviewed analysis: the export's investigation status is in progress and no finding is marked as edited by a person. Validate every item before this alert is shared beyond the site.

## Slide 2
Safety Alert: Hazira gas terminal condensate release and fire, 2020
A seal that does not match the original specification is a change, not a spare.
An opened pressure joint is not proven until it passes a recorded test to design pressure.
Work that can cause a major release needs a check by someone other than the person doing it.
What happened
On 24 September 2020 condensate vapour escaped from a seal on a 1986 metering skid at a gas terminal, six days after the seal had been replaced. The vapour cloud spread for about…
Why it matters to you
All three learnings apply industry-wide. Any site with legacy pressure equipment, locally bought spares or maintenance run on a work notification alone can hold the same…
What we learned
If the specification for a pressure-boundary part is lost and no role owns it, crews fit whatever part is to hand, and the substitute becomes normal practice.
If no procedure says how an opened high-pressure joint is tested before service, crews use the quickest check, and a weak joint passes.
If a job that can cause a major release is planned like routine work, the fitter's knowledge is the only barrier.
What to check now
Do not return an opened pressure-boundary joint to service until a recorded test to design pressure has passed.
List the pressure-boundary seals on legacy equipment that have no specification on file.
Ask stores whether a pressure-boundary seal can be issued without a specification reference.
Check whether safety-critical maintenance jobs carry an independent check of part, method and test.
Questions for your crew
When you change a seal, how do you know the new one matches the original specification?
What test does a joint you opened pass before it goes back into service, and who sees the result?
Who to contact
Send questions, and what your checks find, to the site process-safety lead.
Learning purposes: not a statutory document · Generated with ProbeMatrix Learnings Coach v2.0.0a7 (open source, MIT) from a ProbeMatrix four-level human-factors investigation. ProbeMatrix by Eyekyam: ashley@eyekyam.com
DRAFT
Notes: A seal that does not match the original specification is a change, not a spare.
Cites: FND-8C0BB623; EVD-8645
An opened pressure joint is not proven until it passes a recorded test to design pressure.
Cites: FND-212DC9B7; EVD-2894
Work that can cause a major release needs a check by someone other than the person doing it.
Cites: FND-A6312B6B; EVD-8645
What happened
- On 24 September 2020 condensate vapour escaped from a seal on a 1986 metering skid at a gas terminal, six days after the seal had been replaced. The vapour cloud spread for about…
Text: On 24 September 2020 condensate vapour escaped from a seal on a 1986 metering skid at a gas terminal, six days after the seal had been replaced [FND-8C0BB623; EVD-8645]. The vapour cloud spread for about 46 minutes before the first isolation valve was closed by hand [FND-322112EE; EVD-6414]. It then ignited at a damaged flameproof light fitting and caused a major fire [FND-CCE6F868; EVD-6916].
Cites: FND-8C0BB623; EVD-8645; FND-322112EE; EVD-6414; FND-CCE6F868; EVD-6916
Why it matters to you
- All three learnings apply industry-wide. Any site with legacy pressure equipment, locally bought spares or maintenance run on a work notification alone can hold the same…
Text: All three learnings apply industry-wide. Any site with legacy pressure equipment, locally bought spares or maintenance run on a work notification alone can hold the same conditions today [FND-2FAB8D51; FND-7C5ED5B3; EVD-8645].
Cites: FND-2FAB8D51; FND-7C5ED5B3; EVD-8645
What we learned
- If the specification for a pressure-boundary part is lost and no role owns it, crews fit whatever part is to hand, and the substitute becomes normal practice.
Learning: If the specification for a pressure-boundary part is lost and no role owns it, crews fit whatever part is to hand, and the substitute becomes normal practice.
Explanation: Locally bought O-rings replaced a slot gasket with no specification, check or approval; the seal fitted on 18 September failed six days later.
Cites: FND-8C0BB623; FND-7A32AC87; FND-89962239; FND-B356F15B; FND-91B45FF9; FND-DA67926D; FND-54180594; FND-82673283; FND-45363DCA; FND-A2048FB8; FND-FFE174D0; FND-A443D288; FND-72A7D26C; FND-CEE4B00B; FND-3746C7B6; FND-42BEF461; FND-D66ACA7B; FND-852B7EC7; FND-DEAA7F90; FND-A3D7D53F; FND-B86F67F0; FND-D40839C1; FND-BC4FD086; FND-23139BF9; FND-EBB66554; FND-B440C1BF; FND-8CE00707; FND-6B3A6492; FND-A0017E28; FND-B56701CA; FND-2B0A49CB; FND-35861FFB; FND-2CEE8915; FND-48C48354; FND-9A8F3D7A; FND-7832DDF6; FND-DE30BD8B; EVD-8645; EVD-1494; EVD-0064
- If no procedure says how an opened high-pressure joint is tested before service, crews use the quickest check, and a weak joint passes.
Learning: If no procedure says how an opened high-pressure joint is tested before service, crews use the quickest check, and a weak joint passes.
Explanation: The joint was pressurised only to operating pressure, with no test to design pressure, and went back online about 46 hours later.
Cites: FND-7C5ED5B3; FND-FD617187; FND-212DC9B7; FND-15279F97; FND-7FA02383; FND-4944554C; FND-FDFA6FF5; FND-1662466D; FND-9174A5B0; FND-611A8BFC; FND-904FCA63; FND-C34A026C; FND-257C1100; FND-137BC719; FND-8ACDE078; FND-5919B328; FND-C4E06264; FND-3AB996FC; FND-86CB3683; FND-491EDE74; FND-50C7319E; FND-B91D4A23; FND-7A10FF70; FND-71EE9734; EVD-2894; EVD-0185
- If a job that can cause a major release is planned like routine work, the fitter's knowledge is the only barrier.
Learning: If a job that can cause a major release is planned like routine work, the fitter's knowledge is the only barrier.
Explanation: No one was assigned to check the part, the method or the test.
Cites: FND-2FAB8D51; FND-A6312B6B; FND-28F8790B; FND-59A2F497; FND-F8C125D5; FND-615DB819; FND-7DF14ADB; FND-31459031; FND-63B6D260; EVD-8645; EVD-2894; EVD-5105
What to check now
- Do not return an opened pressure-boundary joint to service until a recorded test to design pressure has passed.
Hold point: yes
Text: Do not return an opened pressure-boundary joint to service until a recorded test to design pressure has passed.
Cites: FND-212DC9B7; EVD-2894
- List the pressure-boundary seals on legacy equipment that have no specification on file.
Text: List the pressure-boundary seals on legacy equipment that have no specification on file.
Cites: FND-8C0BB623; EVD-8645
- Ask stores whether a pressure-boundary seal can be issued without a specification reference.
Text: Ask stores whether a pressure-boundary seal can be issued without a specification reference.
Cites: FND-2FAB8D51; EVD-8645
- Check whether safety-critical maintenance jobs carry an independent check of part, method and test.
Text: Check whether safety-critical maintenance jobs carry an independent check of part, method and test.
Cites: FND-A6312B6B; EVD-8645
Questions for your crew
- When you change a seal, how do you know the new one matches the original specification?
Question: When you change a seal, how do you know the new one matches the original specification?
Why it matters: Shows whether the specification is on file or held only in people's memory.
Cites: FND-8C0BB623; EVD-8645
- What test does a joint you opened pass before it goes back into service, and who sees the result?
Question: What test does a joint you opened pass before it goes back into service, and who sees the result?
Why it matters: Shows whether the test is written down and checked by someone other than the fitter.
Cites: FND-212DC9B7; FND-A6312B6B; EVD-2894
Who to contact
- Send questions, and what your checks find, to the site process-safety lead.
Text: Send questions, and what your checks find, to the site process-safety lead.
Cited records:
FND-8C0BB623: Maintenance Team - Gasket Replacement Without OEM Spec · L1 · rating 4
EVD-8645: document
FND-212DC9B7: Maintenance Team - No Hydrostatic Test After Gasket Replacement · L1 · rating 4
EVD-2894: document
FND-A6312B6B: Gasket replacement unverified maintenance process · L2 · rating 4
FND-322112EE: Gas Terminal emergency isolation MOVs, including MOV 54, supplied as local-manual valves with no remote operation from the control room · L4 · rating 4
EVD-6414: log_record
FND-CCE6F868: Compromised HPMV flame-proof lamp left in service and became the probable ignition source · L4 · rating 4
EVD-6916: physical_item
FND-2FAB8D51: Maintenance job planning for the 18-Sep-2020 gasket replacement on 310FT01 · L2 · rating 4
FND-7C5ED5B3: Maintenance Team - Hydrostatic Test Requirement After Gasket Replacement · L1 · rating 4
FND-7A32AC87: Maintenance Team - Wrong Choice: Substitute O-ring for OEM Rectangular-Slot Gasket · L1 · rating 4
FND-89962239: Gasket replacement using non-standard material - 18 Sep 2020 · L1 · rating 4
FND-B356F15B: Gasket Replacement Procedure - Material Specification Bypass · L1 · rating 4
FND-91B45FF9: Substitute O-ring gaskets without OEM specification or quality control · L1 · rating 4
FND-DA67926D: Meter 310FT01 gasket replacement using locally sourced O-ring instead of OEM rectangular-slot gasket · L2 · rating 4
FND-54180594: Maintenance crew unfamiliar with OEM rectangular-slot gasket specification - Sep 2020 replacement · L2 · rating 4
FND-82673283: Meter 310FT01 gasket replacement — lost OEM specification and uncontrolled O-ring substitution · L2 · rating 4
FND-45363DCA: Maintenance fitters — routine O-ring substitution without authority or qualification · L3 · rating 4
FND-A2048FB8: Hazardous O-ring substitution practice left uncorrected across multiple maintenance events · L3 · rating 4
FND-FFE174D0: Lost OEM gasket specification and uncontrolled local O-ring sourcing never remedied · L3 · rating 4
FND-A443D288: O-ring substitution - regular practice tolerated and modelled by supervisors · L3 · rating 4
FND-72A7D26C: No material specification or procurement policy for pressure-boundary gaskets · L3 · rating 4
FND-CEE4B00B: Meter 310FT01 gasket material practice — no standardized OEM specification/procurement rule · L3 · rating 4
FND-3746C7B6: Maintenance supervision - 18-Sep-2020 gasket replacement of meter 310FT01 · L3 · rating 4
FND-42BEF461: Authorised the locally sourced O-ring substitution as a regular practice · L3 · rating 4
FND-D66ACA7B: Meter 310FT01 gasket material availability - lost OEM spec and locally sourced O-ring substitute · L3 · rating 4
FND-852B7EC7: Material sourcing and gasket specification control on meter 310FT01 not enforced · L3 · rating 4
FND-DEAA7F90: Locally procured O-ring substitution became unwritten standard practice on meter 310FT01 · L3 · rating 4
FND-A3D7D53F: Maintenance crew authorised for the 18-Sep-2020 retaining-plate gasket replacement without OEM specification or pressure-boundary testing competence · L3 · rating 4
FND-B86F67F0: Regular use of locally procured O-rings for the 1986 rectangular-slot meter gasket · L4 · rating 4
FND-D40839C1: Organizational overconfidence in locally procured O-ring substitute as a valid pressure-boundary seal · L4 · rating 4
FND-BC4FD086: Unmanaged substitution of OEM rectangular-slot gasket with locally procured O-ring (18-Sep-2020 repair) · L4 · rating 4
FND-23139BF9: No accountable owner or recorded authority for gasket material specification and procurement · L4 · rating 4
FND-EBB66554: Locally sourced O-ring substitution without specification, QC or recorded authority · L4 · rating 4
FND-B440C1BF: Unassessed program risk of O-ring substitution for OEM rectangular-slot gasket · L4 · rating 4
FND-8CE00707: Accepted 'regular practice' of non-specified locally purchased O-rings as substitute seals · L4 · rating 4
FND-6B3A6492: Locally purchased round O-ring substituted for the OEM rectangular-slot gasket of 1986 meter 310FT01 without specification or QC · L4 · rating 4
FND-A0017E28: Non-OEM locally-purchased O-ring procured as regular substitute for lost 1986 rectangular-slot gasket specification · L4 · rating 4
FND-B56701CA: Lost OEM rectangular-slot gasket specification and no substitute specification/QC information for maintainers · L4 · rating 4
FND-2B0A49CB: Post-gasket-replacement pressure testing procedure · L2 · rating 3
FND-35861FFB: Maintenance staff unfamiliar with the 1986 meter's OEM rectangular-slot gasket specification and substitute O-ring practice · L2 · rating 3
FND-2CEE8915: Flat authority gradient in maintenance material control · L2 · rating 3
FND-48C48354: Maintenance staff not given technical support/mentoring for gasket specification and verification · L3 · rating 3
FND-9A8F3D7A: Maintenance fitter selected for 18-Sep-2020 gasket replacement without current OEM-specification experience · L3 · rating 3
FND-7832DDF6: Maintenance team leadership — pre-incident gasket replacement control failure (17–19 Sep 2020) · L2 · rating 3
FND-DE30BD8B: Management failed to provide any substitute-specification, procurement, or quality-control policy after the OEM gasket specification was lost · L3 · rating 4
EVD-1494: document
EVD-0064: physical_item
FND-FD617187: Maintenance Team - No Hydro-Test Requirement Ignored · L1 · rating 4
FND-15279F97: Post-maintenance testing - 18 Sep 2020 gasket replacement · L1 · rating 4
FND-7FA02383: Post-Maintenance Gasket Replacement - 18-Sep-2020 · L1 · rating 4
FND-4944554C: Pressure boundary work returned to service without hydrostatic test · L1 · rating 4
FND-FDFA6FF5: No hydrostatic test performed after the 18-Sep-2020 gasket replacement · L2 · rating 4
FND-1662466D: Meter 310FT01 returned to service with locally sourced substitute O-ring gasket and no hydrotest · L2 · rating 4
FND-9174A5B0: No SOP for calibration and taking back in service of high-pressure meters — 18-Sep-2020 gasket replacement · L2 · rating 4
FND-611A8BFC: Omitted hydrostatic test and absence of SOP for high-pressure meter return-to-service · L3 · rating 4
FND-904FCA63: Failure to enforce hydrostatic test and return-to-service SOP after gasket replacement · L3 · rating 4
FND-C34A026C: No formal procedure/intent communicated for post-gasket testing and return to service · L3 · rating 4
FND-257C1100: No standard operating procedure existed for calibration and return-to-service of the high-pressure meters, including mandatory hydrotest to design pressure · L3 · rating 4
FND-137BC719: No SOP for calibration and return-to-service of high-pressure meters · L3 · rating 4
FND-8ACDE078: Omission of post-replacement hydrostatic test not identified or corrected before meter return to service · L3 · rating 4
FND-5919B328: Authorised return-to-service without the mandatory hydrostatic test · L3 · rating 4
FND-C4E06264: Post-repair hydrostatic test requirement not enforced on 18-Sep-2020 gasket replacement · L3 · rating 4
FND-3AB996FC: Return-to-service after gasket replacement without design-pressure hydrostatic test · L4 · rating 4
FND-86CB3683: Overconfidence that operating-pressure pressurization validated the repaired pressure boundary without a hydrostatic test · L4 · rating 4
FND-491EDE74: Return of meter 310FT01 to service after 18-Sep-2020 gasket change without design-pressure validation · L4 · rating 4
FND-50C7319E: No post-maintenance hydrotest or return-to-service SOP for high-pressure meter gasket work · L4 · rating 4
FND-B91D4A23: No SOP for high-pressure meter calibration/return-to-service and no OEM gasket specification · L4 · rating 4
FND-7A10FF70: Metering-skid maintenance workspace left without specifications, SOPs, or checklists · L3 · rating 4
FND-71EE9734: Post-maintenance testing shortcut - operating-pressure-only modelled as the norm · L3 · rating 4
EVD-0185: log_record
FND-28F8790B: Maintenance material & quality verification roles not assigned · L2 · rating 4
FND-59A2F497: Maintenance supervision led 18-Sep-2020 gasket replacement beyond equipment/material capability (no OEM gasket, no specification, no hydrotest) · L3 · rating 4
FND-F8C125D5: Pressure-boundary maintenance ordered without independent QC/inspection manning · L3 · rating 4
FND-615DB819: Maintenance job manning for the 18-Sep-2020 gasket replacement · L4 · rating 4
FND-7DF14ADB: 18-Sep-2020 maintenance team lacked QC/engineering oversight in composition for high-pressure pressure-boundary work · L3 · rating 3
FND-31459031: Gasket replacement cross-monitoring failure — 18 Sep 2020 nonstandard gasket and skipped hydro test · L2 · rating 3
FND-63B6D260: No JSA/formal risk assessment for the 18-Sep-2020 gasket replacement · L3 · rating 4
EVD-5105: document

## Slide 3
Coverage
This pack cites 72 of 436 relevant findings.
64 of 150 top-rated relevant findings cited.
Learning purposes: not a statutory document · Learnings drafted by an AI agent from AI-assisted findings
Generated with ProbeMatrix Learnings Coach v2.0.0a7 (open source, MIT) from a ProbeMatrix four-level human-factors investigation. ProbeMatrix by Eyekyam: ashley@eyekyam.com
Learning purposes: not a statutory document · Generated with ProbeMatrix Learnings Coach v2.0.0a7 (open source, MIT) from a ProbeMatrix four-level human-factors investigation. ProbeMatrix by Eyekyam: ashley@eyekyam.com
DRAFT
Notes: This pack cites 72 of 436 relevant findings.
64 of 150 top-rated relevant findings cited.
Learning purposes: not a statutory document · Learnings drafted by an AI agent from AI-assisted findings
Generated with ProbeMatrix Learnings Coach v2.0.0a7 (open source, MIT) from a ProbeMatrix four-level human-factors investigation. ProbeMatrix by Eyekyam: ashley@eyekyam.com
Limits of this pack:
- The alert carries the three priority-1 learnings the engine chose by default (alert-grade); the register holds eight more priority-1 learnings, on emergency response, isolation, gas detection, hazardous-area equipment and competence.